Radio Systems Engineering
a pocketqube story

---
Unicorn 1 Radios for Alba Orbital
Unicorn 1 Radios for Alba Orbital
Experimental System to demonstrate link closure from LEO to GEO
LEO typ 450km
GEO 36786km
Possible: S band operation, 1W transmit power, LORA modulation and very low data rates (< 1kb/s)

---
Approx. 191 dB path loss
Approx. 191 dB path loss
LEO ~450km
GEO 36786km

---
Fortunately the GEO satellite was a
“bent pipe”
(GEO Receive S band, relay to earth in K band)
This means we only need consider closing the link between LEO orbit and GEO orbit
And not the total path back to earth

---
Pocketqube size radio, low power, low cost
  - Limits the radio design
  - Limits choice of components
- Low power limitations
  - Limited Transmit power and thermal issues
- Low cost limitations
  - COTS components
To meet all three criteria, it becomes necessary to use highly integrated radio solutions

---
And …
The project aim was to demonstrate use of LORA in space communications

---
LORA
LORA
Short for Long Range
Semtech Corporation’s implementation of Chirped Spread Spectrum (CSS)
A special case of Spread Spectrum
A family of radio transceivers capable of FSK, GFSK,OOK and LoRa

---
Source:electronics-notes.com

---
Source:electronics-notes.com

---
Source: Digikey notes

---
2.25 GHz S band operation
2.25 GHz S band operation
There is no “highly integrated” transceiver on the market that covers the non-IOT or non-Bluetooth/WiFi bands
    - I.e. Above 1020 MHz, and outside 2.4GHz-2.5GHz
- Frequency must be translated (mixed)
  - Spurious emissions response
  - Power
  - Size
  - Cost